Transionspheric Badge ECR 01

25 Apr 18

Changes to schematic and layout due to feedback from prototype build:

    1. Ground flood at bottom of board isolated.
    2. U2 footprint too narrow.
    3. Wrong footprint at Q1.
    4. Mirror “insert brains” bottom silkscreen by SD card connector.
    5. R6 and R7 silkscreen swapped.
    6. P1 should be at zero degrees, not 45.
    7. Add three fiducials to bottom layer per CM.
    8. C24 220pF, C25 DNS.
    9. Add pull-ups to P1 SDA and SCL lines.
    10. Add protection circuitry around P1.
    11. Add alternative 0.1” switch pads in parallel with S6.